## Slide 1: Descriptors: Detecting Interest Points, attributing them with descriptors and and matching them
Søren Olsen
D E P A R T M E N T O F C O M P U T E R S C I E N C E U N I V E R S I T Y O F C O P E N H A G E N
Notes: Forelæsning: 32

## Slide 2: Plan for today
Recap of interest point detection
Which type of interest point is best
Descriptor construction, SIFT
Matching, i.e. how to compare descriptors

## Slide 3: Recall: Linear scale space
The scale space of I is a 1-parameter family
Scale is given by and is an important parameter in CV algorithms
As the scale increases details in the image disappear and we focus on the large scale structures that are left.
Notes: At scale sigma=0 we have the original image

## Slide 4: Recall: Detecting blobs by Laplacian of Gaussian filter
Finding extrema in 2D:
  Find points that are simultaneous extrema in the x and y direction.
  We can solve this in one go by looking for extrema of the Laplacian of Gaussian filter
  Bright blob: Dark blob:
Discrete implementation: Extrema search in 2D
  Bright blob: than all neighbor pixels
  Dark blob: than all neighbor pixels
  4-neighbors or 8-neighbors
  Keep only blobs where threshold value
Notes: In principal we should look for points of zero gradient – these are all candidate points
The Laplacian (2nd order derivatives) tell us if it is a local maxima or minima.
By looking for local extrema of the Laplacian we are reducing further the amount of detected points.
Next year: Stress that the + in the Laplacian is pixelwise – matrix addition (they are not confident with matrices).

## Slide 5: Interest point detectors: Multi-scale Laplacian blob detector
Finding extrema in scale-space:
  Due to blurring, the Laplacian response decay over scale – solution: Use scale normalization.
  Scale normalized Laplacian:
  Bright blob: Dark blob:
Discrete implementation: Extrema search in 3D
  Bright blob: than all neighbor pixels
  Dark blob: than all neighbor pixels
  6-neighbors or 26-neighbors
  Keep only blobs where threshold value
Notes: The max. response of Gaussian derivative filters decay with scale because of blurring / averaging. We can compensate for this by scale normalization.
Blurring lowers the contrast of the image (squeezing), by multiplying by the scale level we increases the contrast appropriately (stretching).
Next year: Try to improve the arguments for scale normalization.

## Slide 6: Interest point detectors: Detecting Laplacian blobs (fixed scale)
Notes: Gray scale intensities to make it easier to see if a blob is bright or dark
Yellow: Dark blobs
Red: Bright blobs
Scale = 4

## Slide 7: Interest point detectors: Detecting Laplacian blobs (multi-scale)
Notes: Circle radius is equal to detection scale

## Slide 8: Interest point detectors: Detecting blobs by Difference of Gaussians (DoG)
Difference of Gaussians (DoG) is an approximation to the Laplacian of Gaussian filter
Either subtract Gaussian filters prior to filtering or subtract filtered images.
As before look for extrema in
In a multi-scale setting compute the scale space images with factor k increase in scale and search for extrema in scale space. Can be combined with a Gaussian pyramid for increased processing speed.
Notes: k is a scaling factor

## Slide 9: Multi-scale versus multi-resolution: The Gaussian pyramid
Notes: This is simply an implementation of scale space taking advantage of the reduction in detail
Next year: Consider adding a bit more details here: E.g. subsample by taking every second pixels after Gaussian blurring.

## Slide 10: Interest point detectors: Detecting Harris corners (fixed scale)
Find max. of

## Slide 11: Interest point detectors: Detecting Harris corners (multi-scale)
Find max. of
Notes: Again search for maxima in scale-space (in 3D)

## Slide 12: So which detectors are the best?
Kim S. Pedersen DIKU, Anders Dahl and Henrik Aanæs from DTU
Interesting Interest Points.
International Journal of Computer Vision, 97:18 – 35, 2012
We Want to Control it All in a Systematic Way

## Slide 13: Method: Play Around with Robots 

## Slide 14: Method: A Configurable Computer Vision Workbench
Notes: Actually the lamps are not used, instead an array of LED spot lights are used

## Slide 15: Our Analysis: Investigate the recall rate of Interest Point Detectors
Detectors used:
Harris and Hessian Corner Detectors Mikolajczyk & Schmid 2004
  Plain
  Laplace
  Affine
MSER Matas et al. 2004
Intensity & Edge Based Regions Tuytelaars & Van Gool 2009
Fast Corner detector Trajkovic & Hedley 1998
DoG Lowe 2004
Implementations downloaded of the net
Notes: A potential match: If one or more points in the other image pass the 3 tests a match is counted for the point in the key frame.
Total Interest Points: Total number of interest points detected in the key frame.
Recall rate must be high

## Slide 16: Evaluation Criteria: Determining the Correctness of a Match
Epipolar line
Epipole
Baseline
Epipolar plane
Notes: Epipolar Geometry: Epipoles can be outside image plane.
Epipolar Line: A potential match in the other image must be within 2.5 pixels orthogonally on the epipolar line formed by the optical centers and the point in the key frame.
Surface geometry: The detected 3D points should lie close to the ground truth surface. Match consistent with the true geometry of the scene.
Absolute Scale: We want to see the same patch of 3D surface in both images, hence the detectors should localize interest point across scale

## Slide 17: Effect of position
Notes: Results averaged over all 60 scenes.
DoG and fixed scale Harris does well, except fixed scale Harris performs poorly over scale.
Multi-scale Harris actually perform quite well (/not included).

## Slide 18: Outline of First Stage Findings
Light is more disruptive than position (angle & scale).
Best Performers are:
  Harris Variants
  DoG (SIFT Blobs)
  MSER
  Hessian Laplace Variants
Observations:
  DoG (SIFT Blobs) is much better than Hessian Laplace.
  Plain Harris is better than extensions, when scale does not change.
  FAST is very erratic wrt. to number of features.

## Slide 19: Matching Strategy Illustrated
Extract interest points: Harris corners, DoG (blobs)
Compute feature descriptors: Raw patches, , SIFT,…
Match points by pairing similar descriptors
Notes: Find potential matches – in principal we can have several candidates

## Slide 20: What do we wish of a descriptor
We have to attribute each feature point a descriptor to compare if the a candidate match is good or not.
Descriptors have to be local, informative, insensitive to noise, luminance variations, perspective deformation including rotation, to pixel quantization etc.
We like compact (low dimensional) descriptors but recognize that high dimensional ones may be more discriminative.

## Slide 21: Matching patches
?
Notes: Is patch F1 similar to patch F2?

## Slide 22: Using raw pixel patches as descriptors
Represent a patch with the raw pixels – the patch is the descriptor.
Compare patches pixel by pixel, e.g. by (For simplicity lets assume gray scale intensities and the sums are over all pixels in the patches.) (Patches must be of equal size)
This is referred to as either distances or dissimilarity measures
Notes: Not similarity measures because we want them to have small values for similar patches and large values for dissimilar patches.

## Slide 23: Using raw pixel patches as descriptors
We need to compensate for changes in illumination conditions, because …
Contrast change a and change in brightness level c (affine model):
We want F’ and F to have zero distance, but
Invariance wrt. affine intensity changes by normalization:
Notes: The affine model of intensity distortions is not a completely realistic model, but is a good approximation.
Normalization: So how do we pick a and c?

## Slide 24: Matching patches: Normalized cross correlation
Compute mean intensity and standard deviation for each patch (sum over all n pixels in patches)
Measure distance with normalized cross correlation
Affine intensity invariance:
Notes: Subtract mean to remove additive constant and divide by variance to remove multiplicative contrast change factor. Standard deviation is a good measure of the contrast in a patch – It measures the spread of intensities in the patch.
Can also be interpreted as the angle (dot product) between the two patch vectors.
NOTICE next year: Wikipedia has a mistake in NCC where the sum term is divided by n which gives that NCC is not zero. I have removed this in the equation

## Slide 25: Matching patches
?
Raw pixel descriptor: Use pixels in patch and compare with Normalized Cross Correlation
Notes: Is patch F1 similar to patch F2?

## Slide 26: Open problems
What patch size should we use?
  Use the detection scale and resample so both patches have equal size in pixels
Is this approach robust to scale changes in the scene?
  Yes, if we do the resampling (see above)
Is this approach robust to rotation in the scene?
  No, this will lead to large dissimilarities
Is it robust to perspective distortions?
  No, this will lead to large dissimilarities

## Slide 27: Scale Invariant Feature Transform (SIFT)
SIFT is a very popular descriptor (Google. Scholar says 21528 citations Nov. 2013).
Scale invariance:
  This is obtained by using the DoG blob detector which is multi-scale. Descriptor build at these interest points in scale-space.
  After detection we have an interest point at
Rotational invariance:
  Estimate an orientation of the interest point and build the descriptor relative to this.
Translational invariance:
  To some extend by construction of the descriptor (more on this)
Illumination invariance:
  By construction of the descriptor (more on this)
Notes: SIFT is popular and performs well, so lets go into details of what it does.
Several implementations available, but also patented.
16599 citations Nov. 2012

## Slide 28
SIFT
Notes: This is the overview – lets go into details with each step.
Orientation assignment is not even on this chart

## Slide 29: SIFT: Rotational invariance by orientation assignment
At detection scale compute image gradients
Gradient orientation and magnitude images
Build a 36 bin orientation histogram for neighborhood around
  Every point weighted with m and a Gaussian window
for all points in the image
Notes: In SIFT Lowe find the closest scale level in the Gaussian pyramid and compute gradients using pixel differences.
The gradient measures changes in light. The gradient vector points uphill in direction of steepest ascent.
Draw on whiteboard a black and white pattern and point at zero gradient and high gradient areas.

## Slide 30: SIFT: Rotational invariance by orientation assignment
Find highest peak and its orientation
Create an interest point descriptor using this orientation
For all other peaks larger than 80% of the highest peak – also create a descriptor using these orientations
degrees
Notes: High peaks mean that we have many gradients pointing in this direction and / or very large gradients. Example: There is an edge near the interest point so its orientations will dominate.
Highest peak is at 170 degrees
Only the peak at 200 degrees is above 80% of the 170 degree peak – height 10

## Slide 31
SIFT descriptor
Gradient images
8-bin histograms
Orientation image
Notes: The paper suggest 16x16 pixel initial patches, but it can be larger.
8 bin orientation histograms (45 degrees bin width)
4x4 grid of histograms
Orientation image uses pseudo colors to show orientation angle.

## Slide 32: The SIFT descriptor: Details
8-bin orientation histograms:
  When adding to bin, every data point is weighted with m and a Gaussian aperture window
  Adding a data point to a bin also add a little to the neighboring bins (linear interpolation)
  Pixels on the other side of a histogram grid border contributes a little to the histogram (linear interpolation)
Feature vector:
  Concatenate 8-bin histograms from the 4x4 grid into one vector with dimensionality 4x4x8 = 128.

## Slide 33: The SIFT descriptor: Details
Normalization of feature vector:
  Normalize the feature vector:
  Non-linear illumination changes (e.g. shadows) may cause high gradient magnitudes locally.
  Therefore reduce all bin values larger than 0.2 down to 0.2.
  Renormalize (normalize again):

## Slide 34: SIFT matching:
SIFT features are compared with Euclidean distance (L2-norm):
Matching SIFT features:
  A match is accepted if
  Best refers to the distance for the pair of features with smallest distance.
  2nd Best refers to the distance for the pair of features with second smallest distance.
Notes: The sum runs over all the 128 dimensions of the SIFT feature.
Matching: The best match needs to be significantly better than other matches. Best distance <= Next_Best distance hence r <= 1.
This criterion is more stable than just using Best.

## Slide 35: The SIFT descriptor invariance’s
Scale invariance:
  From the (DoG) detector and further processing done at detection scale
Rotational invariance:
  From the orientation assignment procedure
Approximate translational invariance:
  From the grid of histograms. Can handle translations up to 4 pixels (within a grid cell).
Affine illumination invariance:
  From the choice of gradients additive brightness invariance is obtained. From normalization we obtain invariance to multiplicative contrast change.
  Reduction of peaks gives some robustness to non-linear changes such as shadows.

## Slide 36: Open problems for SIFT descriptors
Perspective distortion, but may be extended to become affine invariant
Non-linear illumination such as cast shadows, changes to light color, and material reflection properties
It is fairly high dimensional (128 dim.) and redundant
It is computational intensive and relies on a careful implementation

## Slide 37: Variations on SIFT
There are many variations of the SIFT descriptor:
  GLOH
  SURF
  DAISY
  PCA SIFT
  Opponent SIFT
  Gaussian opponent SIFT
  CSIFT
  ORB
  BRISK
  FREAK
  …
Notes: And many more with even more exotic names

## Slide 38: DAISY – a common SIFT variation: Locations and spread of histograms
Notes: Notice that DAISY is actually not using histograms but instead splits gradients to positive and negative parts.

## Slide 39: What is the best detector and descriptor combination?
Much work has been done
Results are not conclusive
Example from work by Kim S. Petersen, Anders Dahl and Henrik Aanæs using the DTU robot data set

## Slide 40: Detector - Descriptor Combination
Notes: We look at all combinations of detector-descriptor from these tables (A matrix study)
Some descriptors work on color images.
Notice also the large variations in descriptor dimensionality

## Slide 41: Evaluation Criteria
Extract features from the Key frame and another frame.
Matching criterion: Same as before except no scale
Compute: r = Best / 2nd Best < T
Compute ROC and AUC.
Use AUC as performance measure (average over scenes).
Notes: Threshold T on distance ratio r and throw away all points larger than the threshold. Best <= Next_Best hence r <= 1
In ROC we change r to produce the curve.
In assignment 1, what I suggest you try is r < 0.8 and other threshold values.

## Slide 42: Aside: ROC and AUC?
Receiver operating characteristic (ROC):
  TPR = TP / P (Recall)
  FPR = FP / N
Area under the ROC curve (AUC):
  AUC close to 1 is good
  The probability of a correct match
From Wikipedia 2012
Notes: ROC: Performance summary of binary classifiers (Match or No Match):
Confusion matrix: Summary of frequencies of different types of errors performed by the classifier.
TPR (True Positive Rate): Sensitivity or Recall. Ratio between true positives and all positives. Perfect classifier TPR = 1.
FPR (False Positive Rate): 1-specificity. Ratio between false positives and all negatives. Perfect classifier FPR = 0.
Random guess: Equal amount of False positives and False negatives errors.
As we vary r we get a curve (Draw example on whiteboard).

## Slide 43: Results at a Glance, Descriptors
Notes: Each curve represents a descriptor. The blue curve is Raw patch.
AUC averaged over scenes and interest point detectors.
The race is close – most descriptors have close to equal performance!

## Slide 44: Outline of Findings
All SIFT based descriptors have almost equal performance.
Multi-scale Harris is the top performer.
With detectors the devil is in the details.
Light is very challenging.
On statistical significance…

## Slide 45: Quote on Statistical Significance
A question often overlooked by the computer vision community when comparing results on a given dataset is whether the difference in performance of two methods is
statistically significant.”
M. Everingham, L. Van Gool, C. K. I. Williams, J. Winn, A. Zisserman
“The PASCAL Visual Object Classes (VOC) Challenge”
International Journal of Computer Vision, Volume 88, Number 2,
page 303--338, 2010

## Slide 46: Literature
Reading material:
Lowe IJCV 2004 (Sec. 5 – 7.1)
Dahl-Aanæs-Pedersen 3DIMPVT 2011
Aanæs-Dahl-Pedersen IJCV 2012
Additional material:
  Larsen et al ECCV 2012
  T. Lindeberg 1996 (Multi-scale detection)
  T. Lindeberg. Feature detection with automatic scale selection. International Journal of Computer Vision 30(2): 79 – 116, 1998.
Notes: Next year: Consider to include the ECCV 2012 paper as part of the lecture.

## Slide 47: Mandatory assignment 2: Feature extraction and matching
Build and experiment with interest point detectors
Find matching points between two images